## Slide 1
Machine Learning for Predicting Sediment Particle Size Distributions
Mini-project: predict d50 and σ² from environmental measurements
Team members: ____________________ and ____________________
Course / Section: ____________________

## Slide 2
1. Why are we solving this?
Sediment particles constantly aggregate and break apart; this is called flocculation.
Particle size affects settling behaviour and sediment-transport modelling.
Goal: predict two particle-size properties from measurements of the surrounding water and flow.

## Slide 3
2. Dataset
Reference dataset: 1,648 co-located observations from three South San Francisco Bay field campaigns.
Particle-size distributions were measured using a LISST-100x.
Inputs: salinity, wave-induced velocity, particle index of refraction, temperature, optical ratios, chlorophyll-a and tidal velocity.
Targets: d50 (median particle diameter) and σ² (distribution variance).

## Slide 4
3. Our ML approach
This is a supervised regression problem because both outputs are continuous numbers.
Step 1: use Random Forest to estimate feature importance.
Step 2: use the four features selected in the reference project: S, ub, np and T.
Step 3: train Random Forest and compare it with Support Vector Regression (SVR).

## Slide 5
4. How Random Forest works
Build many decision trees instead of relying on one tree.
Each tree sees a slightly different sample of the training data.
Every tree predicts d50 or σ².
The forest combines the tree predictions into one final prediction.
It also gives feature-importance values.

## Slide 6
5. Evaluation
Random Forest: 70% training data and 30% test data, with 32 trees.
SVR: 70% training, 15% validation and 15% test.
Metrics: R², MAE and RMSE.
R² measures agreement with the observed values; MAE and RMSE measure prediction error.

## Slide 7
6. Reference results
The reference study reported Random Forest R² = 0.81 for d50 and 0.75 for σ².
It reported SVR R² = 0.76 for d50 and 0.76 for σ².
These numbers are reference-study results, not results from the included synthetic demo.
Our final results should be generated from the actual dataset provided for the class.

## Slide 8
7. Demo: what the code does
Load CSV → check columns → remove missing values.
Calculate feature importance.
Train Random Forest and SVR.
Predict d50 and σ² on held-out data.
Calculate R², MAE and RMSE.
Save feature-importance tables and true-vs-predicted plots.

## Slide 9
8. Limitations & future work
A model trained in one region may not generalize to another region.
The reference report itself identifies generalization as an important next question.
Future work: add more locations/campaigns, test cross-location performance, tune hyperparameters and examine whether important features remain stable.

## Slide 10
9. Conclusion
Machine learning can model nonlinear relationships between environmental conditions and sediment particle properties.
Random Forest provides both predictions and feature-importance information.
SVR provides a useful comparison model.
The final claim should be based on results obtained from the actual project dataset.

## Slide 11
10. Q&A cheat sheet
Why regression? → The targets are continuous numbers.
Why Random Forest? → It captures nonlinear relationships and provides feature importance.
Why SVR? → It is a second regression method for comparison.
Why train/test split? → To check performance on unseen data.
What is d50? → Median particle diameter.
What is σ²? → Variance/spread of particle sizes.
What is R²? → A measure of how well predictions explain variation in the measured target.